## Slide 1: Comparing Stochastic and Ray‑tracing Datasets in Machine Learning for Wireless Applications
Contributors
João Morais
Dr. Akshay Malhotra
Shahab Hamidi-Rad
Prof. Ahmed Alkhateeb
Asilomar, October 27, 2025
Are stochastic datasets all we need?
Notes: Hi everyone. My name is Joe-Ow, I’m the first author of this paper where we compare stochastic and ray-tracing datasets for ML in Wireless.
I think this is one of the rare times where all co-authors of a paper are present in the same session. This should lead to the most accurate presentation of this work, because they will all be able to correct me if/when I overstep.

## Slide 2: Motivation & Problem
Currently: Stochastic channel models (3GPP TDL/CDL/UMa) are widely used
  For how long? ~ 10-20 years
  Why?
  Reason 1: Standardized
  Reason 2: Reproducible & Scalable
  Reason 3: Sufficient for the time
Problem: New ML applications → Need for site‑specific propagation models
Cost: Stagnant ML research, stuck working with unrealistic data
Alternative: Raytracing (proxy for real) → All benefits, but not standardized
2
How to Decide Between Stochastic and Raytracing Models?
Notes: Let’s start with status quo and the problem we are trying to solve.
(click1)
Currently, Stochastic channel models like 3GPP TDL/CDL/Urban Macro/Micro are the most common source of data for wireless algorithms.
- They have been around for 20 years.
- (click2) Why
- (click3) And they are still very used for several reasons:
- They’re standardized, and in wireless we like and trust standards.
- They are reproducible and scalable - you can set seeds and generate as much data as you want.
- When they were introduced, they were mostly sufficient. Link and System-level simulations worked well.
(this was fine, until) (click4) We came up with... New tasks, (like Beam Management, Localization, ...) that require site-specific propagation models with spatial and temporal consistency.
(what’s the cost of ignoring this problem?) (click5) If we overrely on stochastic, our research efforts may be wasted in fitting to wrong data, solving the wrong problems.
(click6) ALTERNATIVE: (Of course, there is an alternative, which is ray tracing. It recently became much easier to use, but it is not standardized.
(click7) QUESTION: How do we decide between stochastic or RT data?

## Slide 3: Study Questions & Scope
Q1: Does stochastic provide realistic performance expectations?
If not, we need ray tracing
Q2: Is stochastic data useful for pre-training?
Scope:
  1. (1) Overview Stochastic / Deterministic Channel Models and their assumptions
  2. (1) Choose tasks where assumptions match and not match requirements
  3. (4) Train ML models for each task using stochastic and Raytracing datasets
  4. (4) Is stochastic sufficient? Is it useful for pretraining?
3
Notes: 3 Questions and How we plan on solving them
(click1) Q1: If we train/evaluate only on stochastic data, do the results hold on site‑specific RT data?
(click2) Q2: When is RT necessary? In those cases, what’s the role of stochastic?
(click3) Q3: How to choose/combine channel models for a given ML task?
(click4) To solve them, we will:
1- Overview briefly the existing channel models and their assumptions
2- Choose a task where assumptions are sufficient, and one where they are probably not
3- Train models for each task
4- Compare the models to determine whether stochastic data is sufficient, and, when it is not, if it’s useful at all.

## Slide 4: Families of Channel Models: Determinism Continuum
Purely stochastic → spatial channel models → map‑based ray tracing
Path (large-scale) parameters: fixed-clusters → cluster distributions → scene-informed → scene-dependent
4
How Path Parameters are Derived Determines Model Consistency
Notes: Let us start with an overview of Channel models in wireless, organized in a scale of determinism.
- The less deterministic are the purely stochastic (AWGN/Rayleigh), then the spatial models (TDL), then the more geometry‑aware (CDL/GBSM) and finally the map‑based RT (with deterministic reflection, diffraction and scattering equations that give us clear propagation paths)
(click 1) In the paper we include a more detailed taxonomy of these models if you’re interested. For now, it is important to point out that models must derive path parameters from somewhere. They may have pre-defined values for the clusters (TDL/CDL), or distributions (UMa) from which to extract these values - making UMa theoretically much more diverse than CDL. Or other ways of changing parameters consistency (GBSM), or 100% dependent on the scene.
(click 2) The way path parameters in the channel equation are derived determines the “consistency” of the model.

## Slide 5: Modeling Choices that Affect Machine Learning
Consistency across:
  Time–frequency consistency
  Spatial consistency & multi‑user correlation
  Array manifold & near‑field
  Materials & scene sensing
Different ML tasks have different consistency requirements
5
When Stochastic Models CAN / CANNOT Fulfill Task Consistency Requirements, How Does it Reflect in ML Models?
Notes: When we talk about Consistency we are talking about how channels reflect variations in X?
(C1) Temporal consistency (variations in time)
(C2) Spatial consistency (two users next to each other interfere?)
(C4) Array consistency
(C5) Materials and scene geometry
(click 5) Conclusion: Consistency Inscreases with Determinism (Lower: variability/diversity. ) We may not ALWAYS need ray tracing, but

## Slide 6: Machine Learning Task Selection
6
Channel Prediction
Goal: estimate future channel (combat aging)
Requirements: Angle-Delay-Doppler coupled progression
Input: 10‑sample window (single ant & sc)
Output: prediction at horizons {1,3,5,10,20,40} ms
Channel Compression
Goal: reduce signaling overhead
Requirements: Frequency & array consistency
Input: 32 subcarriers x 32 antennas
Output: (same as input, reconstructed)
Notes: We selected 2 tasks:
CSI Compression & (temporal) Channel Prediciton
We chose these two because one the modeling requirements match the models used, and the other do not. So we want to compare networks resultant from training with different channes. (to see if it’s worth having RT or not)
A quick overview.
(click1)
The goal in CSI Compression is to reduce save overhead by compressing a high dimensional channel measurement before reporting it to the BS. Requirements: consistency across frequency and array elements
Input: 32 subcarriers by 32 antennas
Arch: AE (CSINet+)
Output: (same as input)
(click2)
The goal in Channel Prediction is to estimate future channel (combat aging)
Requires a channel evolution in angle-delay-doppler (but some of the stochastic models ONLY evolve in Doppler (their clusters remain static across time, only the phase rotates)
Input: 10 sample window (1ms between samples) - single antenna & subcarrier - focus on temporal evolution
Arch: GRU-based (common in literature)
Output: 1 sample, at horizions 1-40 ms

## Slide 7: Data Sources & Pipeline
Data Sources:
  Stochastic: Sionna TR 38.901 (TDL/CDL/UMa)
  Map‑based: DeepMIMO RT scenes
Shared preprocessing → Task‑specific models
Normalization for Compression: (in real matrix)
Normalization for Prediction: (all axes)
7
Notes: Now we know the models. Let’s see what data we’ll feed to these models.
(click1) Starting with the data sources
- For stochastic, we rely on Sionna for the TR 38.901 implementations of TDL/CDL/UMa.
- For Ray tracing, we use DeepMIMO scenarios. (examples next slide)
(click2) Both data sources feed to a shared preprocessing stage, where we apply the same task-specific normalization to both data sources and then the normalize data follows to Task 1 or Task 2.
(click3) In particular, the normalizations are a) 0-mean 1-variance for compression; b) simple divide by max for prediction

## Slide 8: Ray Tracing Scenarios in DeepMIMO
ASU (asu_campus_3p5) NY (city_0_newyork_3p5) LA (city_1_losangles_3p5)
8
deepmimo.net
Notes: Some examples of the RT scenarios we used from DeepMIMO.
If you’re not familiar, DeepMIMO has a RT database with more than 100 scenarios, that you can download and use, with the dm package, to generate channels in a few minutes.
We will use these 3 names: ASU, NY, LA
Top: 3D buildings. The red points are potential users. Blue are BS. 80k tx-rx pairs on the first, 50k and 50k on the other two, when we append all BSs.
Bottom: GPS top view (google maps)
Memorize this pointy building and this round building here. This will be important for the next slide

## Slide 9: RayTracing Configuration
Compression: 3 scenes at 1 m spacing;
Prediction: ultra‑dense ASU variant (10 cm base, 1 cm interpolated)
RT interpolation: linear on path params (angles, power, phase, delay)
Reflections/diffractions in both; Scattering only in Task 1; No penetration.
Sequences follow straight‑line tracks with geometry‑consistent Doppler
9
Notes: Some RT configurations:
(click1) Compression uses three RT scenes at ~1 m spatial spacing to cover diverse urban/campus geometries.
(click2) Prediction uses an ultra‑dense ASU variant: 10 cm base grid, interpolated to 10 mm, so consecutive samples are within a wavelength.
(click3) This interpolation is linear on path parameters (per path, angles of arrival and departure, power, phase, delay) - max distance between samples 0.1 m ~ wavelength.
(click4) Physical effects include reflections/diffractions (no penetration in this setup); Doppler per path is consistent with geometry and motion.
(click5) Sequences follow straight lines. Imagine a scan...

## Slide 10: Common & Task Settings
Common: 3.5 GHz, Δf=15 kHz, ULA λ/2, No added noise
More samples for prediction (harder task)
Doppler enabled only in prediction (assume 10m/s speed)
Common Loss/Performance metric: NMSE (dB)
Training (X→X), Cross-testing (X→Y), Fine-tuning (X + 1%Y → Y)
10
Notes: Final slide on simulation configurations. We have common and task specific settings:
(click1) Common: 3.5 GHz carrier, Δf=15 kHz, ULA with λ/2 spacing, no additive noise (focus on intrinsic channel structure).
(click2) We use 200k samples for prediction, 50k for compression
(click3) Doppler is only enable in the prediction task, at ~100 Hz (equivalent to 10m/s at 3.5 GHz)
(click4) Finally, both tasks use the same performance loss (comparing reconstructed vs predicted channels uses still N MSE dB
(click5) Now the results we will show are of 3 kinds. In-domain (we trained and teste on the same channels); or cross-testing (train on X, predict on Y); or fine-tune (we train on X, fine tune on 1% of Y and then predict on the rest of Y)

## Slide 11: Channel Compression – Cross-testing & Fine tuning
In‑domain: CDLs & RT are less diverse than TDL‑C/UMa
Zero‑shot transfer:
  CDLs transfer little (-4dB) | TDL/UMa transfer well (-10 dB)
  RT↔RT transfers best (note: peak is ~-20 dB)
1% fine‑tuning:
  TDL & UMa remain hard targets, but great sources for pretraining
  ~5–8 dB gains off‑diagonal; quickly aligns to target domain!
11
Pretraining can close most of the performance gap!
Stochastic is not a replacement for Raytracing.
Notes: Left is the cross-testing performances, right the fine-tuning. This means: we trained on the name on the row, and tested on the name of the column. The brigther the color, the better the performance.
It’ll be easier as we analyse the results:
(click1) In‑domain: (look across the diagonal) - CDL‑C and RT have (≈-20 dB); TDL‑C/UMa are harder
Zero‑shot:
(click2) - CDLs have very low values when teste anywhere besides in themselves. I.e. too specific. (click 3) UMa/TDL, on the contrary, transfer relatively well to the rest of the row.
(click4) - Interestingly, note the RT corner. They transfer relatively well one to the other,
(click5) Fine-tuning: one can simple look at the patterns: the 2 dark column mean any model tested on TDL/UMa had low performance. And the rest is quite bright, meaning even with 1% fine-tuning, the models obtain great performance quite fast!
(click6) In Summary: a) Stochastic is not a replacement for RT. We can tell the performances vary drastically (they even vary from other RT scenarios! Need to get a similar dataset! b) Pretraining can help a lot and practically close all the performance gap in this transferable task.

## Slide 12: Channel Compression – Value of Pretraining
Train: X + %Y → Test: Y
Pretraining helps most when target data is scarce (Gains exceed 8-10 dB)
Diminishing returns beyond ~1×10⁴ samples;
Best gains from RT pretraining (e.g., NY → ASU). Then UMa, then CDL.
12
Pretraining is Valuable, Especially when Data is Scarse and Datasets Similar.
4 dB
8 dB
10 dB
Notes: Now, imagine we fine-tuned on different amounts of the target data. To understand if pre-training is worth it at all, we compare the performance with that of a model that was not pre-trained. Lower = better performance.
(click1) A) You can read here that the more data is available from the target domain, the better performance is, because all perf. gets better.
(click2) B) By looking at the gap between curves, we see the GAIN from pre-training:
- low budgets (400 samples, gains exceed +8–10 dB) from UMa & RT
- gains decrease with more data, but there still seems to be some gain from pre-training on stochastic first.
(click3) C) The gains seem to be larger for RT, then UMa, then CDL. We didn’t hand pick this RT scenario. If we assume an average similarity, we may get even better performance by finding the right datasets.
(click4) Takeaway: Pretaining is valuable, especially when data is scarce and datasets are similar.

## Slide 13: Prediction – Horizon Behavior
At 1 ms: GRU ≫ sample‑and‑hold a cross all datasets (≈−26 to −28 dB)
By 3–5 ms: stochastic retains better NMSE; RT drops faster early but has flatter tail later
Similar 1 ms scores ≠ similar learned structure; geometry matters beyond short horizons
13
Short ~ Doppler | Long ~ Angle-Delay | Differences Exist.
Notes: Then, the channel prediction results. Here we show the prediction error (NMSE), lower is less error) for different prediction horizions. Different colors are different channel models. TDL, CDL, UMa are somewhat together. The purple cross is RT.
Then the two sets of lines are the sample and hold baseline, where we don’t predict any channel, we simply use the available channel, and the filled lines are the performance of the GRU predictor.
(click1) - Naturally, the lines of the GRU are lower than the sample and hold, showing the models are doing something
(click2) - At very short horizons, performances of RT and stochastic are similar, then RT gets worse, then actually gets better.
- Short horizons are dominated by Doppler. After a while, it’s hard to “derive” how much doppler is in the sample.
- Longer horizons are dominated by angle-delay progressions, which can be easier to learn and slower varying. That’s why the performance reverts to ~1ms.
(click3) Of course, Similar performances don’t mean that the same thing was learned, for that we have to cross-test.
(click4) Main conclusion, there are clear differences. Let’s see how models transfer to one another to understand their differences. We’ll do that at 5 ms, a typical channel prediction horizon. (we will switch to the matrices again, expect 16, 17, 12, 8 along diagonals)

## Slide 14: Prediction – Transfer & Fine‑tuning
Zero‑shot transfer:
  stochastic→stochastic all work well. (Doppler modelled similarly)
  stochastic→RT fails
Fine-tuning (1% target data): gaps shrinks, but remains (e.g., TDL‑A→ASU ≈−3 dB)
14
Prediction Needs RT/GBSM for Realistic Assessment
Notes: As before, the left is cross-testing, the right contains fine-tuning.
Let’s go through them clearly.
(click1) Zero shot transfer (i.e. just testing) shows that stochastic transfer extremely well to each other, out of the box. (much better than before) This is likely because the doppler progression is modeled the same way in all of them.
(click2) Also very interesting, is that stochastic to RT fails (click3) . And RT to stochastic also fails. This suggests that what the stochastic and RT models are learning, is definitely different. Stochastic is not learning angle-delay. And because RT is learned angle-delay, when it may misinterpret samples with only doppler. We could train it with different speeds to fix this. But it’s an interesting result that there’s no relation out of the box.
(click4) When we fine tune, the gap between the models shrinks, but it remains. We see that stochastic -> RT is ~3dB (except CDL which did not learn much). RT-> stochastic went to -1 dB (-4 in CDL)
(click5) Bottom line: realistic channel prediction requires geometry‑faithful data (with angle, delay, and doppler evolutions) during training or at least for adaptation; Stochastic‑only evaluation is unreliable.

## Slide 15: Takeaways
Q1: Does stochastic provide realistic performance expectations?
A1: No, gives unreliable expectations for site‑specific behavior.
Q2: Is stochastic data useful for pre-training?
A2: Yes, if it is sufficiently similar to target in specific task.
  If tasks align, transfers work great.
  If tasks do not align, depends on the amount of target data.
15
Do Not Rely Only on Stochastic
Use Ray Tracing (e.g. via DeepMIMO, Sionna, Matlab, ...)
Notes: (click1) Is stochastic all we need? Nope. Even in tasks where assumptions are acceptable, RT performance is not predictable from stochastic. (Neither is from other RT datasets! Test where it matters!)
(click2) Is stochastic useless? Not at all. Extremely useful for pretraining, in tasks where there is alignment, it always provided a boost. Other tasks depends. Pretraining can help IF there is enough data to fine tune. Otherwise just train directly.
(click3) How to select a channel model by task? Check the table, and question your model assumptions and your task requirements.
(click4) Don’t use just stochastic.
With Ray tracing databases and ray tracing engines open-source and free to use, ray tracing data is as easy as ever to download or generate.
(click5) Make sure to use DeepMIMO, or Sionna, or Matlab, and always check your algorithms with some RT data, as proxy a real-world.
There’s no excuse to not pick stochastic.
The only excuse you may have is that your model works better on stochastic (and god help you if you’re training on CDL)

## Slide 16: Thank you
16
github.com/jmoraispk/StochasticRTcomparison
Email: joao@asu.edu
Notes: That’s it for me. If you’re interested in this code, everything is open-source in this github. Thank you!